## Slide 1: XDOS Ground Station
Internal Technical Review · Rev 1.0 · 03 September 2026
Software Architecture & Design
Ground segment · OBC bridge · CCSDS TC/TM · binary rate-group telemetry

## Slide 2: Agenda
01
Purpose, scope and system context
Why the ground station exists and what it covers
02
System block diagram
Nodes, links, ports and process boundaries
03
Software architecture
The layered C++17 stack and its build targets
04
Telecommand flow, end to end
Operator keystroke to decoded response
05
CCSDS TC / TM frame formats
The Level-2 wire contract, field by field
06
Binary rate-group LUT
Design rationale, data flow and file format
07
Subframe and master-frame layout
Tiers, budgets and the 16-slot cadence
08
Simulation environment & power model
Six subsystem sims and the OBC power FSM
09
Verification status and next steps
What is proven, what remains
Sources: repository docs/, mib/ definitions and the C++17 sources; all figures verified against the working tree.

## Slide 3: Purpose, scope and system context
A single C++17 codebase that commands the spacecraft, models it on the bench, and decodes what comes back
What the system is
A Level-1/Level-2 ground station for the XDOS satellite: an operator CLI, an on-board-computer bridge, and a live multi-process simulator stack that stands in for flight hardware.
Every telecommand and telemetry definition is data, not code — loaded at start-up from the MIB JSON files, so a database revision needs no rebuild.
What it delivers today
Telecommanding of six subsystems over CCSDS TC frames, with per-parameter prompting, spec-ID lookup and a full detail view before anything is sent.
Autonomous housekeeping telemetry driven by a binary rate-group look-up table that is authored on the ground, uplinked, and executed by the OBC with no on-board database.
A flight-realistic power sequence: OBC boot, staggered subsystem switch-on, battery-threshold load shedding and recovery.
Design constraints that shaped it
The OBC must stay database-free — it replays opaque command bytes and copies byte ranges, so all meaning stays on the ground.
The downlink subframe is fixed at 1280 bytes; every telemetry budget is validated at build time, never handled at runtime.
THE BUILD, IN NUMBERS
~19 k
lines of C++17
obc · simulator · src · tests
6
subsystems modelled
EPS · ADCS · GPS · Payload · XLINK-S · UHF
418
MIB message definitions
loaded from mib/*.json at start-up
110
test cases, all passing
1 672 assertions under Catch2 v3
Test figure measured by running ./build/xdos_tests on the current working tree.

## Slide 4: System block diagram
Five cooperating processes on one host; every link is a plain TCP socket, so any node can be replaced by real hardware
GROUND SEGMENT — operator host
ON-BOARD COMPUTER — xdos_obc
SUBSYSTEM SIMULATORS
xdos_gs
Operator CLI — telecommanding
MIB-driven listings, params, decode
xdos_tm_view
Master-frame telemetry viewer
tier-indexed, slot-aligned decode
LUT authoring
rate_group_commands.csv
xdos_lut_csv · [g] composer
EGSE power monitor
umbilical poll — [p] menu
Frame Bridge / Router
prefix + APID routing
CCSDS wrap / unwrap, CRC check
CCSDS TC / TM codecs
TC SOF 1ACF · TM SOF FCA1 (1432 B)
Rate-Group Engine
16-slot tier schedule · poll → memcpy picks
assembles the 1280 B subframe
Binary LUT store
obc_lut_store.bin · CRC-16 verified, hot-swappable
Power FSM
UNPOWERED → BOOTING → SEQUENCING → ON
EPS sim TCP 10010
orbit / SOC / Vbatt engine
ADCS sim TCP 10020
quaternion + PD controller
GPS sim TCP 10030
Keplerian orbit propagator
Payload sim TCP 10040
container + capture server
XLINK-S sim TCP 10050
keyed S-band transceiver
UHF sim TCP 10060
OpenLST transceiver
TCP P = 10000
CCSDS TC / TM responses
TCP P+2 = 10002
master-frame push, 1 Hz
TCP P+3 = 10003
binary LUT uplink (“XLUT”)
TCP P+1 = 10001
EGSE / OBC power status
Native subsystem framing
TCP 10010 – 10060
autonomous polls
P is the OBC routing port — 10000 in simulation, 7000 on the bench; the three side channels are always P+1, P+2 and P+3. Solid lines carry commanded traffic, the dashed line is the rate-group engine polling on its own schedule.

## Slide 5: Nodes, links and ports
Each side channel is deliberately separate so an unprompted 1 Hz telemetry stream can never contend with a command reply
Port | Link | Direction | Carries | Endpoint
P = 10000 | TC / TM routing | GS ⇄ OBC | CCSDS TC frames and their responses — the flight link | xdos_gs ⇄ Bridge
P+1 = 10001 | EGSE umbilical status | GS → OBC | OBC power state during boot and load-shed recovery | PowerMonitor ⇄ Power FSM
P+2 = 10002 | Rate-group stream | OBC → GS | 1280 B subframes wrapped in 1432 B TM frames, once per second | Engine → xdos_tm_view
P+3 = 10003 | Binary LUT uplink | GS → OBC | “XLUT” + u32 length + file bytes; replies OK / ERR | Composer → LUT listener
10010 – 10060 | Subsystem buses | OBC ⇄ Sim | Native subsystem framing, one TCP port per subsystem | Bridge ⇄ six simulators
SUBSYSTEM IDENTITY — spacecraft ID 625 (0x271), shared by the TC and TM profiles so uplink and downlink can never drift apart
Subsystem | APID | Sim port | Native framing prefix | MIB definitions
ADCS | 1 (0x001) | 10020 | 1F 7F <id> … 1F FF | 220 messages · 79 enums
UHF | 2 (0x002) | 10060 | OpenLST framing | 41 messages
EPS | 3 (0x003) | 10010 | 00 <base64 telegram> 01 | 82 messages · 16 PDU channels
GPS | 4 (0x004) | 10030 | AA 44 12 … | 19 messages
Payload | 5 (0x005) | 10040 | [type ¦ cmd ¦ len] + data | 10 messages
XLINK-S | 6 (0x006) | 10050 | product key + event frame | 46 messages
Rate group | 600 (0x258) | — | TM only — master-frame push | n/a — position-indexed

## Slide 6: Software architecture — the layered stack
One static library, xdos_core, carries every layer; the executables are thin shells over it
APPLICATIONS
executable targets
xdos_gs
operator CLI
xdos_tm_view
master-frame viewer
xdos_obc
bridge + engine
xdos_lut_csv
LUT compiler
6 × subsystem sims
xdos_tests
Catch2 v3
SESSION & SUBSYSTEMS
src/session · src/subsystems
Session
shared-link slots
Plugin registry
XLINK codec
keyed auth
CODEC
src/codec
CCSDS TC codec
SOF 1ACF
CCSDS TM codec
SOF FCA1, 1432 B
legacy codec
FRAMING
src/framing
adcs
eps
gps
payload
uhf
xlink
DATA MODEL
src/mib · src/lut
MIB loader
messages, params, enums
Binary LUT builder
+ CSV grammar
LUT format
header · entry · picks
COMMON & TRANSPORT
src/common · src/transport
CRC-16-CCITT
hex / colour
EGSE model
types
socket_compat
POSIX + WinSock
TCP client / server
Dependencies point downward only. Third-party code is limited to a vendored nlohmann/json header and Catch2 v3 for the test target; everything else is C++17 standard library plus the platform socket API.

## Slide 7: Telecommand flow, end to end
Ten steps from an operator keystroke to a decoded, unit-tagged response — every hop length-checked and CRC-verified
UPLINK · ground → on-board computer
EXECUTION & DOWNLINK · OBC → subsystem → ground
1
Select the telecommand
xdos_gs lists every MIB command plus synthesized GET entries for GPS and ADCS telemetry. “?ID” shows the full parameter table without sending.
2
Enter the parameters
One prompt per parameter with a [0] default. EPS channel-mask bytes open a picker that names each bit’s subsystem from the MIB.
3
Build the native frame
The exact bytes the subsystem expects: ADCS 1F 7F … 1F FF, EPS base64 telegram, GPS LOG command, XLINK product key + event.
4
Wrap in a CCSDS TC frame
SOF 1ACF, spacecraft 625, APID, GS-ID, time code, then TC-ID / TC-Len / TC-Data and a CRC-16 over the transfer-frame header onward.
5
Send on the flight link
Length-prefixed TCP write to the OBC routing port P. The session keeps one shared slot so replies stay correlated.
6
Verify and unwrap
The bridge checks SOF and CRC-16 before anything else. Running the OBC with --validate prints a structured per-field report.
7
Route to the subsystem
The inner APID selects the bus; the native frame is forwarded verbatim to the matching port in 10010–10060.
8
Simulator executes
The engine responder answers from a live model — orbit, state of charge, attitude quaternion — not from a canned table.
9
Wrap the reply as TM
A fixed 1432 B FCA1 frame: TM DATA carries the native reply and the GS TC cmd field echoes the originating command.
10
Decode and display
xdos_gs resolves each field by MIB offset and size, applies enums and units, and colours the render by command kind.
the frame crosses the link
Nothing on this path is hard-coded. Command lists, field offsets, enums and units all come from mib/*.json; the frame layout comes from mib/ccsds_tc.json. A database revision changes behaviour without a rebuild — and the same profile drives both directions, so uplink and downlink cannot drift apart.
Steps 3 and 9 are the only places where subsystem-specific knowledge lives; steps 4–7 are subsystem-agnostic.

## Slide 8: CCSDS TC / TM frame formats
The Level-2 wire contract — both layouts are loaded from JSON profiles that share one spacecraft identity and APID map
TELECOMMAND FRAME · uplink · variable length · SOF 0x1ACF
SOF
2 B
TF header
5 B
Packet header
6 B
GS-ID
1 B
Time code
8 B
Anc. len
2 B
TC-ID
2 B
TC-Len
2 B
TC-Data
N B
CRC-16
2 B
CRC-16-CCITT coverage: transfer-frame header → end of TC-Data
Version, bypass and control-command flags, spacecraft ID 625 (0x271) and virtual-channel ID live in the transfer-frame header; the inner space-packet header carries the subsystem APID.
Time code on the uplink is the 8-bit-centisecond CCS variant; TC-ID mirrors the subsystem command ID so a reply can be matched to its command without state.
TELEMETRY FRAME · downlink · fixed 1432 B · SOF 0xFCA1
SOF
2 B
TM primary hdr
6 B
Data field status
2 B
SPP primary
6 B
SPP secondary
11 B
TM DATA
1280 B
GS TC cmd echo
123 B
FECF
2 B
CRC-16-CCITT coverage: TM primary header → end of GS TC cmd
TM DATA is exactly one 1280-byte rate-group subframe. The master-frame and sub-frame counters in the primary header give the ground its slot: SFC mod 16 is the subframe index, SFC div 16 the master-frame id.
Time code on the downlink is the 16-bit-millisecond variant — the one deliberate difference between the two secondary headers; identity and APID map are read from the same profile as the uplink.
Layouts read from mib/ccsds_tc.json and mib/ccsds_tm.json; the TM profile references the TC profile so the two can never disagree on identity.

## Slide 9: Binary rate-group LUT — why it exists
The OBC has no subsystem database; it replays opaque command bytes and copies byte ranges, and that is the whole design
THE PROBLEM
Housekeeping telemetry must be polled continuously and downlinked on a fixed cadence, but the flight computer cannot carry a parser for six subsystem protocols.
Putting names, IDs and field maps on board would mean re-flashing the OBC every time a subsystem database is revised.
The downlink budget is fixed and small — 1280 bytes per second — so what is sent has to be selected byte by byte, on the ground.
THE DESIGN
One binary file tells the OBC three things: which telecommands to replay, which bytes of each response to keep, and where those bytes go in the downlink block.
Its runtime job per selection is a single memcpy — no interpretation, no field names, no IDs anywhere in the file.
All meaning stays on the ground, in the database and in a JSON twin that is never transmitted. Position in the file is the only link between the two sides.
No on-board database
The OBC boots with no table and transmits nothing until a LUT is uplinked or a stored one passes CRC.
Change without re-flashing
Edit the CSV, rebuild, uplink. The engine hot-swaps the running table and keeps its slot phase.
Deterministic and quotable
The same table always produces a byte-identical file, so its CRC-16 signature can be cited in a review.
Fails on the ground, loudly
Unknown names, out-of-range picks and over-budget tiers are rejected at build time, never at runtime.
Consequence of the design: the OBC transmits nothing at all until the ground has told it what to poll — a deliberate fail-silent default.

## Slide 10: Binary rate-group LUT — data flow
From one CSV master list on the ground to a decoded master frame on the operator’s screen
GROUND · authoring and build
Master command list
config/rate_group_commands.csv
tier · tc_id · subsystem · tc_name · picks — row order inside a tier is the entry order
Build and validate
xdos_lut_csv · xdos_gs [g] composer
resolves names against the MIB, merges adjacent picks, checks every tier against its budget
Two artefacts
rate_group_lut.bin + rate_group_lut_bin_gs.json
only the .bin is ever transmitted; the JSON twin keeps names, IDs and the resume state on the ground
UPLINK · TCP P+3 · “XLUT” + u32 big-endian length + file bytes
ON-BOARD · accept and execute
Verify independently
magic · length field · CRC-16 · every entry’s structure
a malformed file is rejected with ERR and the running table is untouched
Hot-swap and persist
obc_lut_store.bin
the engine swaps table mid-flight and re-derives its 16-slot schedule; the sub-frame counter keeps running
Poll and pick
VH every subframe · H per 2 · M per 4 · L per 8
each pick is one memcpy into the tier’s block buffer; a failed poll writes 0xFF over that entry’s ranges
ASSEMBLE · one 1280-byte subframe per second, wrapped in the 1432-byte TM frame (APID 600)
DOWNLINK · decode on the ground
Push to the ground
TCP P+2 · 1 Hz · master frame = 16 subframes = 16 s
SFC mod 16 positions the subframe, so a lost frame leaves a gap instead of shifting everything
Rebuild the blocks
xdos_tm_view
slices VH / H / M / L out of each subframe and reassembles each tier’s block across its span
Name the bytes again
the JSON twin maps block offsets back to commands, parameters and units
the CRC-16 signature proves both sides hold the identical table
The two sides never exchange names or IDs. Position within a segment is the only correspondence, and the shared CRC-16 is what guarantees it.

## Slide 11: Binary LUT — file format, field by field
One 50-byte header, then four segments (VH, H, M, L) of variable-length entries packed back to back; all values little-endian
HEADER · 50 bytes · offset 0
Off | Size | Field | Value / meaning
0 | 4 | magic | “XLUT” — file identifier
4 | 1 | version | 1 — format revision
5 | 1 | flags | 0 — reserved
6 | 2 | subframe_size | 1280 — fixed; the 1362 B variant is ruled out
8 | 2 | seg VH | 400 B
10 | 2 | seg H | 400 B
12 | 2 | seg M | 300 B
14 | 2 | seg L | 175 B
16 | 1 | reserved | 5 — bytes 1275–1279, transmitted as zero
17 | 1 | pad | 0 — alignment
18 | 2 | T_sf | 1000 ms — subframe period (legacy 0 reads as 1000)
20 | 8 | entry counts | u16 × 4 — entries in VH, H, M, L
28 | 16 | segment offsets | u32 × 4 — absolute file offsets, direct seek
44 | 4 | file length | total bytes — integrity check with the CRC
48 | 2 | CRC-16-CCITT | poly 0x1021, init 0xFFFF, whole file with this field zeroed
ENTRY · variable length · repeated per segment
Field | Size | Meaning
sync | 2 | 0xA55A — entry boundary marker
apid | 1 | hardware APID — ADCS 1 · EPS 3 · GPS 4 · Payload 5 · XLINK-S 6
flags | 1 | reserved = 0
tc_len | 2 | length of the TC bytes that follow
tc bytes | var | the complete native frame, replayed verbatim on the bus
tm_raw_len | 2 | raw response payload length, per the database
pick_count | 1 | number of pick triplets
picks | 6×n | the triplets below
PICK TRIPLET · 6 bytes each
Field | Size | Meaning
src | 2 | byte offset in the raw response payload
size | 2 | number of bytes to copy
block | 2 | destination offset inside the tier’s block (generator-assigned)
The OBC’s entire runtime job per pick is memcpy(block + block_off, payload + src, size) — zero interpretation.
Adjacent or overlapping selections merge automatically, so eight flags packed in one byte cost exactly one byte.
Picks are stored by name in the ground-only JSON twin, so a database revision recomputes offsets instead of silently shifting bytes.

## Slide 12: Subframe and master-frame layout
Every subframe carries all four tiers at fixed offsets; the tiers differ only in how many subframes a block spans
ONE SUBFRAME · 1280 bytes · transmitted once per second
VERY HIGH
bytes 0 – 399
400 B
HIGH
bytes 400 – 799
400 B
MEDIUM
bytes 800 – 1099
300 B
LOW
bytes 1100 – 1274
175 B
RSV
ONE MASTER FRAME · 16 subframes · 16 seconds · block boundaries are subframe-aligned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
VH
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
H
block 1
block 2
block 3
block 4
block 5
block 6
block 7
block 8
M
block 1
block 2
block 3
block 4
L
block 1
block 2
A block holds unique data spread evenly across the subframes it spans — 20 400 bytes of unique telemetry per master frame, plus 16 × 5 reserved bytes
Tier | Block span | Unique data per block | Blocks / master frame | Unique / master frame | Current classification | Picked bytes per command
Very high | 1 subframe | 400 B | 16 | 6 400 B | 27 commands | ≈ 14.8 B ← the tight tier
High | 2 subframes | 800 B | 8 | 6 400 B | 18 commands | ≈ 44.4 B
Medium | 4 subframes | 1 200 B | 4 | 4 800 B | 23 commands | ≈ 52.2 B
Low | 8 subframes | 1 400 B | 2 | 2 800 B | 10 commands | 140 B
A tier whose picked bytes exceed its budget is rejected at build time with the tier and the offending entry named; unfilled block bytes are zero-padded.

## Slide 13: Simulation environment and flight power model
The simulators answer from live physical models, so the ground station is exercised against changing values rather than canned replies
SUBSYSTEM SIMULATORS · one process each
EPS engine xdos_eps_sim
Propagates state of charge and battery voltage against the orbit — 3 300 s sunlit, 2 100 s eclipse — with the PDU channel mask setting the load.
ADCS engine xdos_adcs_sim
Propagates an attitude quaternion under a PD controller; set, get and act commands move the modelled body and the telemetry follows.
GPS engine xdos_gps_sim
A Keplerian orbit propagator behind the native message set; LOG commands return position, velocity and time as the receiver would.
Protocol responders payload · xlink · uhf
Structurally correct replies rather than physics: acknowledgement bytes, keyed S-band events and OpenLST transceiver responses.
FLIGHT POWER MODEL · the OBC power FSM
UNPOWERED
bridge drops
every frame
BOOTING
10 s boot,
EGSE answers
SEQUENCING
2 s stagger
per subsystem
ON
watches EPS,
restores loads
kill switch OFF at any point returns to UNPOWERED
Battery mode | Threshold | Channels shed
Full | ≥ 12.0 V | none
Normal | ≥ 11.1 V | none — the default sequence is restored, staggered and rate-limited
Safe | ≥ 9.9 V | Payload (O10)
Critical | ≥ 9.0 V | Payload, ADCS and the avionics bus (O10, O4, O3)
Below critical | < 9.0 V | everything except the two OBC channels (O1, O2)
Hysteresis of 0.15 V keeps a battery sitting on a threshold from oscillating. All timing honours a time-scale factor, so the full boot-and-sequence run compresses into milliseconds for tests while staying real seconds on the bench.
Bindings are by EPS PDU channel ID from the master sheet; the labels come from mib/eps.json and the sequence from config/flight.json.

## Slide 14: Verification status
Measured on the current working tree — ./build/xdos_tests reports all tests passing
110 test cases
1 672 assertions
21 test translation units
100 % passing
Area | Test translation units | What it proves
Utilities | test_crc · test_hex | CRC-16-CCITT against known vectors; hex encode/decode round-trips
Subsystem framing | test_adcs_framing · test_eps_framing · test_gps_framing · test_payload · test_uhf · test_xlink_codec · test_xlink_keys | Native encode/decode round-trips per subsystem, and rejection of malformed or truncated frames
CCSDS codecs | test_ccsds_codec · test_ccsds_tm_codec · test_ccsds_validator | Frame layout, shared identity, both time-code variants, CRC coverage and the structured validator report
Data model | test_mib_load | Every mib/*.json loads; messages, parameters, enums and channel maps resolve as declared
Binary LUT | test_binary_lut · test_binary_rate_lut · test_rate_group_csv | Header and entry encoding, deterministic CRC signature, pick merging, over-budget rejection, CSV grammar and row-numbered errors
Rate-group engine | test_rate_group | The 16-slot tier schedule, block assembly, the 0xFF down marker on a failed poll, and hot-swap while running
Flight behaviour | test_power_sequence · test_flight_realism | Boot and staggered switch-on, load-shed thresholds with hysteresis, and staggered restore on recovery
End to end | test_e2e | Ground station → OBC → simulator → ground station across the real socket stack, not mocks
Not covered by this suite: real flight hardware, the RF layer, and behaviour under sustained link congestion — these need bench time, not more unit tests.

## Slide 15: Status and next steps
The frame layout is final and the binary LUT path is implemented end to end; what follows is bench work and housekeeping
DELIVERED AND VERIFIED
Telecommanding of all six subsystems, MIB-driven, over CCSDS TC frames.
CCSDS TM downlink in the fixed 1432-byte frame, decoded and rendered on the ground.
CSV → binary LUT build, uplink, OBC verification, hot-swap and persistence.
Tier-scheduled polling with a 16-position schedule and slot-aligned master frames.
Flight power sequence with load shedding, hysteresis and staggered restore.
110 test cases covering framing, codecs, LUT, engine, power and one end-to-end path.
PROPOSED NEXT STEPS · for review
Exercise the bench port map (7000-series) against the real OBC, including the LUT listener on 7003.
Bring Payload, XLINK-S and UHF commands into the rate-group classification — today it is dominated by ADCS, EPS and GPS.
Test the LUT in that LUT cover all Telecommands to check the maximum size of LUT and how its handling.
Add remaining subsystem like XLINK-X test the TC & TM. Add Payloads and check the power sequence’s
Add the radio ID, currently backdoor is implemented. UHF RMID, SBAND RMID and BroadCast.
DECISIONS CLOSED · recorded in docs/binary_lut_design.md
Frame layout
1280 B subframe, 400 / 400 / 300 / 175 / 5 — the 1362 B variant ruled out
Subframe period
T_sf = 1000 ms; master frame every 16 s, written into the LUT header
Cadence
Tier-scheduled 16-position schedule, computed by the OBC at LUT load
Execution source
The binary LUT only — the JSON LUT uplink path is retired
Authoring
One CSV master list, compiled by xdos_lut_csv or imported in the composer